## Slide 1: PVC HBM Errors and ECC
Zion Kwok (MIO)
July 10, 2024
Intel Confidential

## Slide 2: Outline
DRAM overview
HBM fault patterns and ECC
HBM Column Soft Errors
HBM Row Soft Errors

## Slide 3: DRAM components
From Samsung: Graphic explanation Bank,Block,Row,Column for Intel_230913.pdf
Wordline
Bitline

## Slide 4: Inside a DRAM chip
From Samsung: Graphic explanation Bank,Block,Row,Column for Intel_230913.pdf
There may be multiple dies in a DRAM package
DRAM dies have peripheral logic for I/O channels, mode registers, etc
DRAM dies have a dense array of cells, each with one transistor and one capacitor that stores charge
The array is divided into bank groups
Bank groups have multiple banks
Banks have row and column address decoders

## Slide 5: Inside a bank
From Samsung: Graphic explanation Bank,Block,Row,Column for Intel_230913.pdf
No money in this bank
Green squares are cell array blocks
Cell array blocks may also be called memory array tiles (MAT)
A row of MATs may be called a subarray
  In this example there are 13 subarrays (L0L12)
Each MAT may have ~1000 rows and ~1000 columns
For each row activate, one row is activated on all MATs in a subarray (row of MATs)
  During a read or write, one row may be activated per bank
  Refresh may choose to activate more rows per bank
Column address chooses some bits from each MAT

## Slide 6: Cell Array Blocks / Memory Array Tiles (MATs)
Sense amplifiers are between rows
  Sense amplifiers store the “page” or “row buffer”
  Sense amplifiers may or may not be shared between MATs above and below
Left and right MATs share subwordline drivers
Row address decoder  one main wordline  multiple subwordline drivers  multiple subwordline arms  cell transistors turned on
Cell capacitors charge/discharge bitline  sense amplifiers detect and maintain logic level
The column address will select e.g. 8 bits from each MAT when reading or writing
8 bits
Read/Write
Subwordline driver
Bitline
Sense amplifier
Subwordline arms
Cell
Page / Row Buffer
MAT
Column Address

## Slide 7: Putting it all together
During a row activate, the row address is transferred: CA pins  bank group  bank  row decoder  one wordline  multiple subwordlines
Subwordlines asserted  cell transistors turn on  cell capacitors charge/discharge bit lines  sense amplifiers detect and maintain logic levels
Column address: CA pins  bank Group  bank  column decoder  column select lines
Column selects subset of sense amplifiers
During a write, data  DQ pins  bank group  bank  selected sense amplifiers  bitlines  cell transistors  cell capacitors
During a read, data from selected sense amplifiers  out of bank  out of bank group  prefetch buffer  DQ pins
From Intel - Samsung[External] Updated DDR6 Die Architecture Rev2.pptx
Prefetch buffer

## Slide 8: What are some common fault patterns?
Single bit errors
  Could be caused by a cell capacitor that leaks charge too quickly
  Sometimes two neighbouring cells have a small short circuit that affects both DRAM cells
  Could be related to channel I/O signal integrity as well
Column faults
  Could be caused by a short circuit or open circuit in the bitline, or just higher resistance
  Could be caused by a defect in the sense amplifier transistors
  Affects multiple row addresses
  Column select line (CSL) faults can affect multiple columns
Row faults
  Subwordline driver or subwordline arms may have a defect
Multiple row faults
MAT faults
  Some other faults could affect a number of cells within a cell array block / MAT

## Slide 9: How do fault patterns relate to ECC codes?
Single bit errors are the most common, and projected to increase significantly in future DRAM generations
DDR5 DRAM components have on-die ECC, which is single-error correction (SEC), which can correct most single bit errors
Row faults are now responsible for a larger percentage of DDR5 DRAM errors
  Pareto of faults varies for each memory supplier, for each process generation, and for each product
  Row and column faults map to DQ and burst patterns: want to group these bits into ECC symbols
Samsung’s HBM2E also has on-die ECC
  Single error correction double error detection (SECDED)
  Stronger than DDR5’s on-die ECC

## Slide 10: Pontevecchio (PVC) HBM

## Slide 11: Mapping of fault patterns to Samsung’s HBM2E
From Samsung: Samsung Response - Intel RAS Review(SPR vs.PVC)_230326.pdf
72 DQ lanes
PVC system ECC can correct one 8DQ x 2burst region

## Slide 12: Samsung’s HBM2E On-die ECC
From Samsung: 2019040_Samsung_Flashbolt_ODECC.pdf
“When a CSL error occurs, and even it is miscorrected, it happens within same CSL, it doesn’t go beyond CSL.”
From Samsung: Samsung Review about Aurora System_240704.pdf

## Slide 13: On-die ECC H matrix
A possible reconstruction of the H matrix:
If there are 2-bit errors, P7 = 0 and P6:P0 != 0000000  OD-ECC UE
If there is a column select line (CSL) fault that affects a group of 8 bits
  If 1 bit error, then SECDED will correct that bit  OD-ECC CE
  If 2, 4, 6, or 8 bit errors, then SECDED will detect P7 = 0 and P6:P0 != 0000000  OD-ECC UE
  If 3, 5, or 7 bit errors: P7 = 1 and P6:P3 will match the value for the group of 8 bits  miscorrect within same 8 bits
If the CSL fault affects OD-ECC parity bits
  If 1 bit error, then SECDED will correct that bit  OD-ECC CE
  If 2, 4, 6, or 8 bit errors, then SECDED will detect P7 = 0 and P6:P0 != 0000000  OD-ECC UE
  If 3, 5, or 7 bit errors: P7 = 1 and P6:P3 can be anything  OD-ECC UE or miscorrect 1 bit with many possible locations
1 CSL

## Slide 14: On-die ECC H matrix
A possible reconstruction of the H matrix:
If there is a subwordline (SWL) fault that affects a group of 16 bits
  If 1 bit error, then SECDED will correct that bit  OD-ECC CE
  If 2, 4, 6, 8, 10, 12, 14, or 16 bit errors, then SECDED will detect P7 = 0 and P6:P0 != 0000000  OD-ECC UE
  If 3, 5, 7, 9, 11, 13, or 15 bit errors, then P7 = 1 and P6:P3 will match the value of one of the two groups of 8 bits  miscorrect within same 16 bits
If there is a subwordline (SWL) fault that affects the OD-ECC parity only
  If 1 bit error, then SECDED will correct that bit  OD-ECC CE
  If 2, 4, 6, 8, 10, 12, 14, 16 bit errors, then SECDED will detect P7 = 0 and P6:P0 != 0000000  OD-ECC UE
  If 3, 5, or 7 bit errors: P7 = 1 and P6:P3 can be anything  OD-ECC UE or miscorrect 1 bit with many possible locations
1 CSL
1 SWL

## Slide 15: Combination of OD-ECC and System ECC
From Samsung: Samsung Review about Aurora System_240711.pdf
* Note that Fault Errors Map corresponds to HBM3, not HBM2E, but other columns are correct.
Our possible reconstruction of H matrix was bounded in SWL

## Slide 16: Failure Summary
These failures exclude early life failures
Collected from 510,000 HBM devices on the Aurora supercomputer over ~3 months
  DPM can be calculated as # failures x 8, but the # failures is strongly correlated to utilization, so some fine tuning is needed
Soft errors contribute a significant portion of failure events (more details in later slides)
The cause of the uncorrectable errors that happen only once is not clear
From Samsung: Samsung Review about Aurora System_240711.pdf

## Slide 17: Recent learnings from PVC HBM debug
Row and column repair enable latches are most vulnerable to soft error events
  This results in correctable or uncorrectable errors that can only be fixed by resetting the DRAM
    Row repair soft errors may look like a die failure case during ECC decoding
  Row repair soft errors can result in reading the wrong address, which will may silent data corruption (SDC) if the ECC codeword is on only one die (e.g. LPDDR, HBM)
    Server CPUs have scrambling based on the address, which should detect most cases
    Vulnerable if scrambling is turned off or if the scrambling is based on column addresses only
When errors are reported from multiple banks, it may be the result of a DQ channel signal integrity issue, and not a soft error

## Slide 18: Column Repair Soft Errors

## Slide 19
From Samsung: The Mechanism of SER CE storm_240502

## Slide 20
From Samsung: The Mechanism of SER CE storm_240425

## Slide 21
From Samsung: The Mechanism of SER CE storm_240418

## Slide 22
From Samsung: The Mechanism of SER CE storm_240418

## Slide 23
From Samsung: The Mechanism of SER CE storm_240418

## Slide 24
From Samsung: The Mechanism of SER CE storm_240418

## Slide 25
From Samsung: The Mechanism of SER CE storm_240418

## Slide 26
From Samsung: The Mechanism of SER CE storm_240418

## Slide 27
From Samsung: Samsung Review about the SDC Possibility_240613

## Slide 28
From Samsung: Samsung Review about the SDC Possibility_240613

## Slide 29
From Samsung: The Mechanism of SER CE storm_240418

## Slide 30: Row Repair Soft Errors

## Slide 31
From Samsung: Samsung Review about the SDC Possibility_240523
 | Master fuse not cut (repair originally disabled) | Master fuse cut (repair originally enabled)
SER on master fuse | Case 3 | Case 1
SER on one of 14 address fuses | Case 4 | Case 2

## Slide 32
From WH Song’s Samsung Redundancy Scheme and Failure Model.pptx

## Slide 33: Row Repair SER will cause SDC
From Samsung Review about SDC Possibility_240621.pdf
From Samsung Review about SDC Possibility_240523.pdf
- All zero data is a correctable codeword for PVC, because scrambling is disabled!
- Memory controller will not detect an error  Silent Data Corruption (SDC)
SDC
SDC