## Slide 1: The Gen AI Opportunity
Pradeep Dubey Intel Senior Fellow and Director, Parallel Computing Lab
April 2024

## Slide 2: AI Problem Statement & the GenAI Opportunity
AI Update:
  Trained on text, image, code or protein … data, AI can now learn a model that generates a novel text, image, code or protein … that is indistinguishable, yet original compared to the training data
     AI’s Dream Moment: claiming to do human minds do every night while dreaming
  We can avoid training-from-scratch for various use cases, and instead cheaply (in cost terms) fine-tune or augment a large model down to a smaller-and-better model for a specific context.
AI Opportunity:
  Above two have significantly sped up the permeation of AI into various content creation and decision-making workflows, which were reluctant in adopting AI so far, simply because of economies-of-scale associated with more machine-and-less-human-cycles in the workflow.

## Slide 3: Intel Opportunity in the Generative AI Era Is this another iPhone moment for Intel?
Compute flops-bandwidth requirements have gone up 100-1000x or more at the high end (pre-training) and 10-100x for the volume server and client as well.
Easier to meet compute flops needs than feed needs
Highest-level manifestation of limitations that could end-it-all:
  Energy cost of sustaining AI compute needs: primarily rooted in cost of data movement
  Developer disconnect: Growing gap of ninja-performance vs. data-scientists
System Asks:
  Compute
  North-South: Feed the compute
  East-West: Scaling up/out
  Packaging it all

## Slide 4: Technologies for AI-27
Baseline
Disruptive ‘27
Disruptive,
Tech readiness at risk for ‘27
HBM4
ADM Gen3
Memory Cube
Organic: 2.5, 3D
Glass substrate (Laurentide)
Low Power Perf. optimization (1280)
VccMin reduction
Power Via++, Power Delivery
1.8KW Single Phase and Pumped Two-phase cooling
PVR, IVR
Top side power delivery
Series power
48V into Module, VR Chiplet
Immersion cooling
(PoC with Omniva, DoE)
LPDDR Extreme Channel count
Optical Interface (GilaBend+, Mystery Bay) (Platform and Silicon Integration ready)
Standards-based scale-up interface
Industry Protocols: UEC/Falcon-Lite/CXL
Ethernet
UXI + PCIe Switches
OEM fabrics
Super reticle expansion
Wafer over Wafer Bonding
High ball-count package
Networking Protocols
(Brad B)
Optical Interfaces
(Matt A)
High Memory
Bandwidth
(Rajat A)
Packaging
(Pooya T)
Process
(Eric F)
Power Delivery (Rich) &
Cooling: (Tejas S)
AI System (Saurabh)
&
Compute (Max)
Software
(AlexH)
Compute: 4b Datatype
Compute: Next-Gen X86 Core
Compute: Next-Gen Xe4 IP
Library based Compiler
Compiled OOB AI performance
AI generated performant code
Integrated System Solutions
(Optimized Xeon + Xe GPU in a scalable Box with NW, Mem, Storage with AI Infra and enterprise platform )
AI27 Core Team: Brad Burres, Mathew Adiletta, Nevine Nassif, Pradeep Dubey, Sailesh Kottapalli, Sundar Balasubramaniam
Workstream

## Slide 5
Credit: Amir Gholami: https://medium.com/riselab/ai-and-memory-wall-2cb4265cb0b8

## Slide 6: AI Today | Dominated by Nvidia
Infiniband Switch
Infiniband Switch
Infiniband Switch
Infiniband Switch
Bluefield
IPU/DPU
Bluefield
CX8 NIC
CPU
CPU
Bluefield
CX8 NIC
Bluefield
CX8 NIC
Bluefield
CX8 NIC
Bluefield
ICX8 NIC
Bluefield
ICX8 NIC
H100
GPU
NVSwitch
NVSWitch
NWSwitch
NVSwitch
Standard Ethernet Datacenter Network (Storage, Tenant VMs, etc)
H100
GPU
H100
GPU
H100
GPU
H100
GPU
H100
GPU
NVLink
PCIe/CXL
UXI
...
...
Each H100 is expected to sell for ~$16k
Each NVSwitch is ~$15k
Each Infiniband Switch is ~30k
DGX H100
DGX H100
DGX H100
...
Nvidia DGX H100 | 
Component | AI Server
CPU | $ 5,200
8 GPU (incl. HBM) | $ 128,000
Networking (8 NICs, 4 NVSwitches) | $ 77,908
Memory | $ 7,860
Storage | $ 3,456
chassis, MB, Cooling, PS | $ 2,586
Assembly & Test | $ 1,485
Markup | $ 42,000
Total | $ 268,495
Networking makes up > 1/3 of the total DGX cost
Credit: https://www.semianalysis.com/p/ai-server-cost-analysis-memory-is

## Slide 7
Credit: https://www.exxactcorp.com/blog/HPC/NVIDIA-H100

## Slide 8: Photonics Based Disruptive AI Networking
Proof of Concept (POC):
  32 Nodes, 256 Falcon Shore 1 (FS1) GPUs
  SLEEK (Electronic IC, Intel designed/architected): TapeOut Q3’24
  Engineering Validation and Testing Q1-Q2’25
Product
  30K+ Falcon Shore 1 GPUs per systems
  2H’26
Collaboration
  Photonics Startup – SoW in place
  CSP Partner – SoW is WIP
Objective By 2026, in collaboration with a definitional CSP partner and a photonics technology provider, deliver a photonics-based networking solution for AI that achieves: a) >3x bisection bandwidth and >2x network power saving under iso-network-capex cost, with respect to contemporary Ethernet; and b) achieves an AI datacenter deployment at a scale of >100K Falcon Shores.