## Slide 1: Accelerating Innovation for Product & Foundry Leadership – System Design Studio
TSLRP leads: Vivek Rajan, Tanay Karnik
TSLRP Fellow Sponsor: Eric Fetzer, Atul Kwatra
TSLRP VP Sponsor: Vinoo Srinivasan, Bob Brennan
TSLRP PM: Sophie Lennon
Core Team: Bala I., Surhud K., Slade M., Rob M., Ravi M., Ram V., Lalitha S., Satish S., Chris R.,…
TSLRP 2023

## Slide 2: Executive Summary
Context
Inflection Points & Threats
Proposed Solution
Co-develop a design studio to accelerate system prototyping and deliver proven STCO solutions
Risks of falling behind in our IDM 2.0 targets
IDM 2.0 requires open platforms & interoperable solutions
Lack of integrated solutions for system-level PPAC analysis
Competition has a head start but we can embrace & extend
3X ↓ in Concept to Engineering Commit time + effort
PPAC: performance, power, area & cost
STCO: system technology co-optimization

## Slide 3: Focus of This TSLRP
A Full System
System Architecture
System Software
Application & Workloads
Software
Cores & Accelerator IP
Chiplets
IPs + Chiplets
Process Technology
Transistors & Interconnect
Foundational IP
Silicon Stack
Advanced Packaging
Packaging
Goals of STCO program are
Translate system needs and bottlenecks into technology requirements
Explore the possibility to enable new architectures leveraging unique software and technology co-design
How to enable Intel and our foundry customers to develop optimal systems is this TSLRP focus
STCO: system technology co-optimization

## Slide 4: A Unique Phase for Intel
Past
1970s
Success built on
proprietary hardware
proprietary solutions
open software
Future
2030s
Future success requires
open platforms
interoperable solutions
unlock partnerships
Present
Intel in a saddle period
Hint: Let us learn from Microsoft’s turnaround strategy…
Q: How do we enable open platforms and unlock partnerships?

## Slide 5: Microsoft’s Turnaround Strategy
Visual Studio: a powerful developer tool that enables you to complete the entire development cycle in one place.
GITHUB: The complete developer platform to build, scale, and deliver secure software.
Microsoft cloud: access, management, & development of applications & services via globally-distributed data centers
Satya Nadella appointed as CEO
2014
Success built on
proprietary OS
proprietary software
proprietary applications
Past
Turnaround enabled by
open platforms
open solutions
partner-first mindset
Future
… this required cultural transformation as well

## Slide 6: Competitive Landscape
….
A Bottom-up & Hardware Centric Approach: Language, Automation, Co-Design
Example: 3DBlox co-developed with AMD; currently being standardized with EDA
3Dblox is a language to model key physical stacking and the logical connectivity information in 3DIC designs in a single format

## Slide 7: Intel has Better Opportunity with Our Assets, But …
Boards
Packages
Chiplets
Full Stack
Cost
Signal Integrity
Power Delivery
Thermal
High Fidelity Solvers
Task Level
Functional
Electrical
Simulations
Partitioning
Co-Simulation
Applications
Interconnect
Components
IPs
(with PnP models)
Library + IPs
Summary of challenges
Proprietary solutions and interfaces
Fragmented solutions
Interoperability issues
Novel idea
Embrace
Interoperable
Issues
Lack of
Standards
Unique Differentiation
ARM, RISCV, ...
FDIO, HDIO, …
EMiB, Foveros,
Unique Solvers for early Tech analysis
Disjointed solvers
e.g, Simics
HW/SW Partitioning
Silo
Static Perf/Watt
… detailed case-study in slides ahead

## Slide 8: To Win, We Must …
ACT
DELIVER
REALIZE
Pervasive benefits to internal products and foundry customers
Embrace industry solutions
An Integrated studio for top-down and end2end system solutions
Extend with Intel differentiation

## Slide 9: Upside of an Integrated Studio
Bolster IFS business
2
Artificial Intelligence
Ubiquitous Compute
Cloud to Edge Infrastructure
Pervasive Connectivity
Sensing
Super-powers
New advanced node customers
CSP
Auto OEM & Tiers
MAG
Full-stack optimization of systems
1
CSP: Cloud Service Provider
MAG: Military, Aerospace, Government
3
Govt. benefits from the same
Public-private partnership
Chiplet platform: enable startups & academics to rapidly innovate and drastically reduce costs

## Slide 10: We Propose … System Design Studio
Customer
Secure repository
System Design Studio
Foundry Customers
Studio for Foundry Customers
1
System Design Studio
Applications
Constraints
Collateral
Libraries
Solvers
HW / SW Systems
Tools
3X↓ in Concept to Engineering Commit time + effort
2
Unique differentiation
Embrace
Embrace + extend
Research
Boards
Packages
Chiplets
IPs
(with PnP models)
Interconnect
Components
stack
Reference Designs
Reference Methodologies
reference
Cost
Signal Integrity
Task Level
Functional
Electrical
Power Delivery
Thermal
tools
Partitioning
Co-Simulation
research
Secure Repositories
Cloud
EDA Solutions
infrastructure
Common representation
… quantification of 3X benefits in slides ahead

## Slide 11: Top-Down System Design Studio Workflow
Novel idea
Embrace
Interoperable
Standard
Compliance
Unique Existing Differentiation
Applications
Workloads
SW Spec
HW Spec
Profiling
SW / HW Partitioning
SW Modules
IPs/Chiplets/Models
SW Libraries
Design Libraries
Analysis Engines
System
Design
Studio
Feedback

## Slide 12: System Design Studio Workflow #1
Applications
Workloads
SW Spec
HW Spec
Profiling
SW / HW Partitioning
SW Modules
IPs/Chiplets/Models
SW Libraries
Design Libraries
Analysis Engines
System
Design
Studio
Feedback
Novel idea
Embrace
Interoperable
Standard
Compliance
Unique Existing Differentiation

## Slide 13: 1a. Common Representation of Hardware
HW Representation
Board
Package
Chiplets
Components
IPs
(Specs + FW)
Parametrized and reuse-friendly library
Full-stack HW representation
Software Defined Hardware

## Slide 14: 1b. System Prototype
Optimized Schematic
Optimized (layout) Design
; ================================
; Compute Chiplet
; ================================
module compute-chiplet :
port system-io : system-io
port ucie : UCIe-interface(UCIe-Advanced)
inst uclane : ucie-module(UCIe-Advanced, 22.0e-3)
net (uclane.ucie ucie)
inst hublane : ucie-module(UCIe-Advanced, 22.0e-3)
net (hublane.ucie ucie)
inst jtag-interface : io-block(jtag(), 55.0e-3)
net (jtag-interface.io system-io.jtag)
place(uclane) at loc(1.0, 0.0) on Top
place(hublane) at loc(-0.75, 0.0) on Top
place(jtag-interface) at loc(-0.0, 0.0) on Top
property(self.shape) = Rectangle(2.0, 2.0)
property(self.thickness) = 0.5
property(self.PDK) = "Intel-18A"
property(self.RTL) = "compute.vl" ; some model - composed of smaller models
layer(Courtyard(Top)) = property(self.shape)
schematic-group(uclane) = compute-1
schematic-group(hublane) = compute-2
Characterized and parametrized component
; ================================
; Board (full system)
; ================================
module board :
port system-io : system-io
inst IntelProc : package-board-interface(0.6, Top)
net (system-io IntelProc.system-io)
net GND ()
inst dimm : DDR4-dimm/component[4]
for i in 0 to 4 do:
place(dimm[i]) at loc(0.0, to-double(i) * 9.0) on Top
require ddr : DDR4-interface from dimm[i]
net (system-io.ddr4 ddr)
net (dimm[0].VDD dimm[i].VDD)
net (dimm[0].VPP dimm[i].VPP)
net (GND dimm[i].VSS)
schematic-group(dimm[i]) = (Ref(to-string("DIMM-%_" % [i])))
inst P1V8 : components/ADP3336ARMZ/module(1.8)
inst P3V3 : components/ADP3336ARMZ/module(3.3)
inst J1 : ocdb/components/belfuse/SS-52400-003/component
inst USB-PD : components/STUSB4500QTR/module ; USB-C PD device
net (J1.vbus USB-PD.Vbus)
net (J1.CC1 USB-PD.CC1)
net (J1.CC2 USB-PD.CC2)
require ctrl:i2c from USB-PD.U1
net (system-io.sys-i2c ctrl)
inst flash : components/AT25SL321-U/module
place(IntelProc) at loc(0.0, -15.0) on Top
property(self.shape) = RoundedRectangle(200.0, 70.0, 1.0)
Characterized and parametrized system

## Slide 15: 1c. New Intermediate Representation for Design Exploration
Design requirements & goals in code
Data-sheets
Supply chain data
Design validation
Export CAD files
System SW, Firmware configuration
Test Plan
ESIR
Library
Std. Interfaces, components, …
Solvers
Placement
Routing
Signal Integrity
Thermals
Power Delivery
ESIR
Design #1
Design #2
Design #3
Optimization goals
…
ESIR
ESIR
ESIR
ESIR: Electronic Systems Intermediate Representation
Design space exploration
ESIR is an open standard: https://github.com/JITx-Inc/open-components-database/blob/main/README.md

## Slide 16: System Design Studio Workflow #2
Novel idea
Embrace
Interoperable
Standard
Compliance
Unique Existing Differentiation
Applications
Workloads
SW Spec
HW Spec
Profiling
SW / HW Partitioning
SW Modules
IPs/Chiplets/Models
SW Libraries
Design Libraries
Analysis Engines
System
Design
Studio
Feedback

## Slide 17: 2a. Solvers for Design Space Exploration
Mechanical
Electrical
Thermal
Cost Modeling
One Design Representation  Multiple Solvers
Bump and wire sizes
Bonding footprint
xyz constraints
Thermal / temperature characteristics and constraints
Power delivery
Noise margin
Capacitance
Predict PCOS
Democratize real-time cost prediction
https://unitcost.intel.com/
Integrated Solvers for System Prototyping and Cost Analysis

## Slide 18: 2b. Integrated Simulators for Modeling and Co-design
Leverage and unify a set of existing models/simulators
Cross-domain PnPnT Modeling & Dynamic Simulation
Support Continuous integration and deployment (CI/CD)
Used from architecture pathfinding to SW validation
Simics HW/SW Co-design and validation
Micro arch simulators: Microarchitectural tuning
Emulation, FPGA, RTL hybrids : Silicon Readiness to SW
CoFluent Architecture exploration
Docea
Power, performance and thermal tuning
Workloads (SW function)
Validated SW & architecture

## Slide 19: Research Directions for System Design Studio
Novel idea
Embrace
Interoperable
Standard
Compliance
Unique Existing Differentiation
Applications
Workloads
SW Spec
HW Spec
Profiling
SW / HW Partitioning
SW Modules
IPs/Chiplets/Models
SW Libraries
Design Libraries
Analysis Engines
System
Design
Studio
Feedback

## Slide 20: Explore HW Bindings for AI/ML Algorithms
https://people.eecs.berkeley.edu/~ysshao/assets/papers/vaesa-ispass2022.pdf
AI / ML Dataset
System Design Studio
….
SW
design space exploration
large design space ~ 1017
optimized network
System = Chiplets + Software
Achieves 5% more efficient system design

## Slide 21: With AI & LLM Every Studio User Can be a Power User
Faster iterations
Example: Generate new design ideas and explore different configuration options
Reduce errors
Example: Flag potential issues with specification in system context
↑ Optimization space
Example: Suggest system improvements and help make tradeoffs

## Slide 22: Use Cases
Use Cases
1. TTM acceleration for Internal products
2. Bolster IFS business
3. Platform enablement for government programs

## Slide 23: Case Study #1: Product STCO Analysis
System
Concept
Model
1
RAYS
hours
ROT
mins
PCOS
days
ChSolver
hours
Cost
Model 2
Simics
mins
Docea
hours
Martini
hours
Marlin
hours
KPI
Model 3
Perf
mins
Keiko
days
Avalanche
weeks
IDPA
weeks
TCO
hours
PnP
Model 4
Scalars
days
SimTools
weeks
RedHawk
weeks
Clocking
weeks
SITools
weeks
Electrical
Model 5
Floorplan
months
Thermals
weeks
Physical
Intel
EDA
For detail map and description of see here
M11
M12
M13
M14
M21
M22
M23
M24
M31
M32
M33
M34
M41
M42
M43
M44
M51
M52
M45
M35
The challenge: developing systems requires evaluating many options
High-expertise within and cross domains
Does not scale
Breaks down for IFS customers
To address: need methodology with following pillars
Common (plug-able) model
Studio - easy to use, extensible
Built on industry standards
Action: System Design Studio
Develop or embrace common model
Co-develop the Studio
Leverage existing Industry solutions
STCO: system technology co-optimization
Notes: The challenge: developing systems requires evaluating many options
Problems (within & cross-domains) built on high-expertise
Does not scale to large # of options or evaluating new opportunities
Breaks down for IFS customers
To address: need methodology with following pillars
Common (shareable) model of different views (plug-able by others)
A studio, can be used by anyone (easy to use / debug; extensible)
Built on open / industry standards
Action: System Design Studio
Develop or embrace common model
Co-develop the Studio
Leverage existing Industry solutions

## Slide 24: System Design Studio Benefits
System
Concept
M1
Unified Cost Analysis
Cost
M2
Integrated Architecture Exploration
KPI
M3
Integrated Microarchitecture Exploration
TCO
PnP
M4
Multi-Physics Early-Analysis Engine (SI, PI, Reliability)
M5
Software Defined Generators
Physical
Intel
EDA
Common
Model
Current System Design | With System Design Studio
Model Creation | Days | Minutes
Analysis | Minutes | Minutes
Model Creation | Hours | Hours
Analysis | Hours | Hours
Model Creation | Weeks | Days
Analysis | Days | Minutes
Model Creation | Weeks | Days
Analysis | Days | Hours
Model Creation | Month | Days
Analysis | Days | Hours
Embrace Industry Solution & Extend
A studio: easy-to-use, resource optimized
Electrical
Notes: Reduced resource requirement

## Slide 25: Case Study #2: Thermal Challenge
Focused
2-week redesign
effort with Si Experts
Original proposal to customer
Tj,max,die1 = 130 oC
Tj,max,die2 = 125 oC
TDP = 81.4 W
Tamb = 88.5 oC
Thermal/architecture co-designed solution
Tj,max,die1 = 120.5 oC
Tj,max,die2 = 120.7 oC
TDP = 80.7 W
Tamb = 88.5 oC
Results from 2-weeks of Thermal/Silicon co-optimization: “un-selectable” → “winning the race on thermal”
Current Methods built for relatively slow optimization times!
Target by end of 2023, optimization can be done in ~2 days
System Design Studio Target: by end of 2024, optimization can be done in ~2 hours
Notes: Refloorplan and some IPs redesigned

## Slide 26: Case Study #3: Optimal Silicon Partitioning for Foundry Customer
DDR Chiplet
DDR Chiplet
IO Chiplet
Compute Chiplet
IO Chiplet
Cost Contributions | Monolithic (Intel18A) | Compute (Intel18A) + DDR/IO (Intel3) | All Chiplets (Intel18A)
PCOS ($/u) ± 1σ @ISO 685 | High | Low-1 | Low-2
Silicon Cost Contribution | High % | Medium % | Medium %
Packaging And Test (PAT) Cost Contribution | Low % | Medium % | Medium %
Advance Packaging Cost Contribution | N/A | < 10% | < 10%
Scrap Cost Contribution | < 5% | < 10% | < 10%
Comparative / pairwise analysis for any homogeneous or heterogeneous implementations

## Slide 27: Case Study #4: Platform Enablement for Government Programs
Upcoming USG Program | Description
NAPMP | Advanced packaging manufacturing
CHIPS | Chips for America
3D-PRODIGY | 3DIC-Physical design, validation, architecture
Secure repositories and studio for semiconductor solutions
Proven components, Chiplets, and IPs to jump start grand challenges
secure access
repositories
government
programs
System Design Studio
with proven solutions

## Slide 28: Overall System Design Studio Value Thesis
Accelerate Time to Leadership
Proven STCO Solutions
STCO Optimization
Intel ® Simics®
Firmware Accelerated
Validation Accelerated
Robust Products
Architecture
Performance
Intel® CoFluent™
Thermal
Intel® Docea™
Development Accelerated
Mechanical
Cost
Bring heterogeneous parts to market, faster, with better PPA & yield
STCO: system technology co-optimization

## Slide 29: System Design Studio Development Plans
System Design Studio
EDA Collaboration
Example: https://www.cadence.com
Looking for strategic partnership [pending discussion]
Niche start-ups with significant potential
Example: https://www.jitx.com
Lead driver of co-development: https://intel.com
Intel’s role: drive strategic alliance and use-cases for IDM 2.0
University collaboration
Focus: research directions
Example: https://stanford.edu [App Store]

## Slide 30: Our Approach will Drive Increasing Value
Approach
Assumptions
Risks
Continue Status Quo
Heterogenous Systems will organically grow
Participate in the ecosystem
Our competitors (TSMC, AMD, …) leapfrog us
Participation
Partner w/ Govt
Incubate & accelerate grand challenges
Intel assets are key for system challenges
Competition acts faster seeing ↑ benefits
Partnering
All-In
Prioritize holistic studio for systems
Massive benefits, leapfrog competition
Culture & externalization challenges
Leading

## Slide 31: Call To Action
TD
SATG
DEG
IFS
Partnership
Near Term: 1 year
Develop Studio Tech
Enable APIs for Systems Solvers
Unify a set of existing models/simulators
Embrace 3DBlox
Adopt common-model (ESIR)
Certify reference designs & methods
Confirm strategic EDA partner
Medium Term: 1 – 2 years
Acceleration
Offer proven recipes for co-design
Release an always-alive architecture models
Intercept pathfinding of 2026 products
Pilot use cases with IFS customers
Develop Studio monetization streams
“Going forward, the focus is going to be on the methods and tools that help enable STCO.” – Ann Kelleher, EVP, Intel Corporation
Long-Term: 4+ years
Strategic Innovation
Develop generators for predictive process kits
Automate SW-HW Partitioning
Introduce AI + LLM for System exploration
Establish an App store for Systems
Link: Natural Language Guided Si Product Development
Notes: Who will lead and thy have to work together
COE formation

## Slide 32: Acknowledgements & Sub-Teams
Relation to past TSLRPs
  [2021] Silicon at the Speed of Software – SiFive presentation
  [2021] Compiler Inspired HW Design
  [2022] Open-Source Silicon Stack
Current 2023 TSLRP
  Natural Language Guided Product Development: Advance Intel AI-ification by assessing future potential of LLMs + Intel data to streamline E2E development
Team | Leads, Partners
Core Team | Vivek Rajan, Tanay Karnik, Bala Iyer Eric Fetzer, Atul Kwatra, Vinoo Srinivasan, Bob Brennan, Mark Doran Ravi Mahajan, Satish Surana, Lalitha Immaneni Rob Munoz, Shubha Bommalingaiahnapallya Surhud Khare, Slade Morgan Ram Viswanath, Chris Rothstein
Studio Sub Team | Rajiv Mongia Mark Doran Nanda Kuruganti Jin Yang
Product Fit Sub Team | Slade Morgan, Surhud Khare Takuya Abe
Business / Market / Ecosystem Sub Team | Rob Munoz Bob Brennan Ram Viswanath, Al Fazio Global Supply Chain Team
Long Range Sub Team | Mahesh Subedar, Desmond Kirkpatrick, Fadi Aboud

## Slide 33: BACKUP

## Slide 34: STCO Tools Details
LTD RAYS (PF Si Cost)
Hours
Standalone system
Excel + JMP
ATTD RoT (PF PAT Cost)
Mins
Standalone system
Web UI
LTD + MPE + Finance (PK-PRQ PCOS)
Days
Standalone system
Excel based
Chop Solver (SKU stack)
Hours
Standalone system; ongoing integration w/ RAYS
Software Optimizer
Cost Analysis
Analytical Perf Model for broad workloads (PF)
Mins
Integrated with Avalanche for power-constrained perf (V/F)
Excel
Keiko/Coho/IWPS
Days
1C/cycle accurate/full-system simulators
Software models
Avalanche (Bin-Split/PnP)
Weeks
Integrated with analytical model for perf CPI inputs
Software automation
IDPA (Power)
Weeks
Integrated with Avalanche
Software automation
TCO Model
Mins to hours
Standalone system
Various versions from excel to python-based tool
PnP Analysis
Floor-planning
IPs
  Die
  3DIC
  Package
Weeks-Months
Standalone systems
Thermal
Physical Analysis
Process scalars
Days
Standalone system
PDK block scaling
APR analysis by PESG TFM
3DIC integration models
Weeks
D2D IO/TSV/IP Scaling
Circuit simulations tools
Power Delivery (platform/PKG/3DIC)
Weeks
Standalone system
Bedspring (PF)
Red Hawk
Clocking
Weeks
Standalone system
Circuit simulations tools
Signal Integrity
Reliability
Electrical Analysis